## Slide 1: NETWORKING
By.Harsha Vardhan.S

## Slide 2: What is networking? Networking is the process of connecting computers, servers, and other devices to share data, resources, and services. PAN:-personal area network LAN:- local area network WAN:-wide area network MAN:-metropolitan area network CAN:-campus area network

## Slide 3
DAIGRAM of PAC
PAN:-PERSONAL AREA NETWORK

## Slide 4: LAC:- local area network
A Local Area Network (LAN) connects computers and devices within a limited geographic area like a home, school, or office building. It allows resources (like files, printers, and internet) to be shared among multiple devices.

## Slide 5: WAC:- wide area network
A Wide Area Network (WAN) is a telecommunications network that extends over a large geographic area — such as a city, country, or even globally. It connects multiple LANs (Local Area Networks) together using leased lines, satellites, or the Internet.

## Slide 6: MAN:-Metropolitan area network
A Metropolitan Area Network (MAN) covers a larger area than a LAN but smaller than a WAN — typically a city or a large campus. It connects multiple LANs within a city or metropolitan region, often using high-speed infrastructure like fiber optics.

## Slide 7: CAN:-campus area network
A Campus Area Network (CAN) is a type of computer network that connects multiple LANs within a limited geographic area, such as a university campus, business campus, or military base. It's larger than a LAN but smaller than a MAN and typically privately owned.

## Slide 8: IP ADDRESS

## Slide 9: IPV 4:-
IPv4 (Internet Protocol version 4)
Format: 32-bit number (e.g., 192.168.1.1)
Written as: Four decimal numbers separated by dots
Range: 0.0.0.0 to 255.255.255.255

## Slide 10: IPV6
IPv6 (Internet Protocol version 6)
Format: 128-bit number
(e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334)
Written as: Eight groups of four hexadecimal digits
Supports: 340 undecillion (3.4×10³⁸) addresses

## Slide 11: TOPOLOGY

## Slide 12
Topology | Cost | Reliability | Scalability | Use Case Example
Bus | Low | Low | Poor | Small office LANs
Star | Medium | High | Good | Home networks, schools
Ring | Medium | Medium | Poor | Some WANs, token ring LANs
Mesh | High | Very High | Excellent | Military, high-security
Tree | Medium | Medium | Good | Enterprise networks
Hybrid | High | High | Excellent | Large organizations

## Slide 13: BUS TOPOLOGY:-
Structure: All devices are connected to a single central cable (the "bus").
Pros:
Easy to set up
Cost-effective
Cons:
Failure in the mainable crashes the network
Difficult to tubleshoot

## Slide 14: STAR TOPOLOGY:-
Star Topology is one of the most common and widely used network topologies, especially in homes, schools, and small to medium businesses.
Feature | Benefit
Easy to install | Simple setup with minimal cabling
Easy to troubleshoot | Problems can be isolated to one link
Reliable | Failure in one cable doesn’t affect the rest
Scalable | Easy to add or remove devices

## Slide 15: RING TOPOLOGY:-
Definition and Structure
A ring topology is a type of network configuration in which each device (or node) is connected to two other devices, creating a closed loop or circular structure. This arrangement allows data packets to travel in one direction (unidirectional) or both directions (bidirectional) around the ring. In a unidirectional ring, data flows in a single direction, while in a bidirectional ring, data can flow in both directions, enhancing reliability.
Pros:
  Equal access for all devices
Cons:
  A single break can bring down the network
  Slower than star topology

## Slide 16: MESH TOPOLOGY:-
Structure:
Every device is connected to every other device.
Pros:
Highly reliable
Redundant paths
Cons:
Expensive and complex

## Slide 17: TREE TOPOLOGY:-
Structure:
A combination of star and bus topologies
Pros:
  Scalable
  Easy fault detection
Cons:
  Main hub failure brings down the network
.

## Slide 18: HYBRID TOPOLOGY:-
Structure: Mix of two or more topologies (e.g., star + ring).
Pros:
  Flexible and scalable
Cons:
  Expensive and complex to maintain

## Slide 19: OSI MODEL

## Slide 20: OSI LAYERS:-

## Slide 21: Physical Layer Transfers raw bits over the physical medium Cables, electrical signals, fiber optics Data Link Layer Handles MAC addresses, switches, and frame delivery Detects and corrects errors in physical layer Network Layer Handles logical addressing and routing IP addresses, routers Transport Layer Ensures reliable transmission of data Manages error checking, retransmissions

## Slide 22: Session Layer Maintains communication sessions Opens, uses, and closes sessions between systems Presentation Layer Translates data between the application and network Handles encryption, compression, and encoding Application Layer Closest to the end-user Provides network services like email, browsing, etc.